## Slide 1: SAFE HANDLING OF TRASH
Presented by: Dr. Ed Griswold
Safety Specialist
La. Tech Office of Environmental Health and Safety

## Slide 2: OBJECTIVES
Identify the types of trash that you may encounter in trash receptacles.
Describe the potential hazards posed by different types of trash.
Describe the proper methods for handling and disposing of trash.
Describe the methods you should use to reduce injuries, particularly injuries to the back that can result from lifting trash

## Slide 3: Type of Trash Encountered at the University
General Waste
Chemical Waste
Biological Waste
Universal Waste
Items That Are Not Trash

## Slide 4: General Waste
What is it?- Paper, Plastic, Drink cans, Food and Food Wrappers, un-Contaminated glass, Floor Sweepings and other misc. materials
Potential Hazards: None, EXCEPT, “ YOU CAN NEVER BE SURE WHAT IS INCLUDED IN THIS TRASH”!!!!!!
PROTECTIVE MEASURES: Follow the General Rules for handling trash.

## Slide 5: Chemical Waste
What is it: Chemical waste is any chemical material that is for disposal, and includes both hazardous and non-hazardous chemicals.
Potential Hazards: Most chemicals can cause some degree of damage. This damage may be a chemical burn, or damage to lungs, if inhaled; or may catch fire.
Protective Measures: Custodial or Grounds are not to handle containers of chemical that are found in the trash or are “set out” for disposal. These personnel are to contact their supervisor if they observe such a situation.

## Slide 6: Biological Waste
What is it: This is any materials of biological origin or materials that have been contaminated with this material. This includes animals, animal parts, un-sterilized culture plates, blood-collecting/storage equipment
Potential Hazard: May be infectious, comes in contact with cuts or mucous membranes.
Protective Measures:
1. All biological material must be sterilized or separately bagged in a “biohazard” bag by the user. Biohazard bags are red with the “Biohazard symbol”
2. Contaminated “sharps” such as needles must be placed in puncture-proof containers by the user. The Office of Environmental Safety is responsible for disposal of un-sterilized materials and of “sharps”.
3. Custodial or Grounds are not to handle containers of biological waste that are found in the trash or are “set out” for disposal. These personnel are to contact their supervisor if they observe such a situation.

## Slide 7: Universal Waste
What is it?- Universal waste is generally defined as batteries, mercury-containing lamps and other mercury-containing items, circuit boards, old pesticides.
Potential Hazards: All are potentially dangerous to the environment and humans.
Protective Measures: It is University Policy that none of these items are to be discarded in General Waste. The Office of Environmental Safety is responsible for disposal of these items. Custodial or Grounds are not to handle these items that are found in the trash or are “set out” for disposal. These personnel are to contact their supervisor if they observe such a situation.

## Slide 8: What do You do With Items That are Not Trash?
Often, items that are not trash are thrown away in the trash by accident. “Just because it looks like trash and smells like trash, doesn’t always mean that it is trash.
Teachers sometimes set items on trash cans or in halls that are not necessarily trash.
Please ask your supervisor when you have a question as to whether something may or may not be trash and NEVER throw away any item in question.
YOU WILL NEVER BE REPRIMANDED FOR SAVING AN ITEM IN QUESTION!!!!

## Slide 9: GENERAL SAFETY RULES WHEN HANDLING TRASH
Always wear puncture-resistant gloves when handling bags of trash.
Do not wear open-toes or cloth shoes. They will not protect you against chemical spills or cuts from sharp objects to the foot.
When picking up trash, bend your knees slightly and use nearby desk or furniture to provide additional support with your free hand.
Never reach down into a trash can to pull out a bag. Either lift the can or the bag out of the can.

## Slide 10: GENERAL SAFETY RULES WHEN HANDLING TRASH
5. NEVER USE YOUR ARMS OR LEGS TO PUSH DOWN TRASH TO MAKE ROOM, USE ANOTHER SAMLLER CAN OR A PUSH STICH TO DO THIS.
6. Small can bags can be placed into larger bags, but large bags should never weigh more than 25 pounds.
7. Suction/vacuum problems often occur when trying to pull bags from a can. Tip the can or poke a hole in the top of the bag to avoid this problem.

## Slide 11: GENERAL SAFETY RULES WHEN HANDLING TRASH
8. Bags leaking fluids or in danger of bursting should be double bagged
9. Push barrels or carts; don’t pull them, except when going through doors, unassisted.
10. When moving trash, be aware of your surroundings so you do not trip over objects.
11. When handling bags of trash, always hold the bags away from your body. The bags may contain objects that are sharp or other materials that can puncture/penetrate the bag and injure you.

## Slide 12: GENERAL SAFETY RULES WHEN HANDLING TRASH
12. Make sure the lids of top-loading dumpsters are securely propped open before attempting to throw trash into the dumpster. Be careful of handling dumpster lids in high wind. It may swing back and injure your hands.
13. Never attempt to hoist bags of trash or other items into a dumpster if they seem to be too heavy for you to handle. Always call on a colleague to assist you in this task.
14. When throwing bags into a dumpster from a cart, don’t twist from the waist. Instead move your feet, and change directions with your entire body.

## Slide 13: GENERAL SAFETY RULES WHEN HANDLING TRASH
15. Make sure your hands are out of the way when closing dumpster lids
16. If a dumpster is full, securely tie the bags and leave them by the dumpster.
17. Never climb on or into a dumpster.

## Slide 14: SUMMARY
REMEMBER:
“ACCIDENTS DON’T JUST HAPPEN”
TO PREVENT THEM:
YOU are the one who must know the proper way to perform your tasks!
YOU are the one who has to follow the rules!
YOU are the one who is in the best position to recognize an unsafe condition!
YOU ARE responsible for your own safety!
IF YOU DON’T KNOW, ASK!!!!!!!!